## Slide 1
object distance calculation
camera
location
Camera x
Field of View, α
α
pixels in x (e.g. 320)
object pixels
Object angle, θ
θ
Known quantities: camera FoV (α), camera resolution (pixels along x), object width w
Image analysis gives you object pixels
Calculate θ ≈ α * (object pixels / x resolution)
Calculate tan θ/2 ≈ (w/2) / d  d ≈ (w/2) tan(θ/2) (will be in same units as w)
w
d
θ

## Slide 2
object center and rotation
Camera x resolution (e.g. 320)
Corresponds to field of view, α in degrees
0,0
x
y
cv coords
x,y
cv2.boundingRect(contour) returns x,y,w,h
x,y: top left pixels of rectangle
w is width, h is height
e.g. 280, 80, 61,59
object center is (x+w/2, y+h/2)
One way (no if statements) to rotate to center on the object, we let our target x go from -1 to 1: target_x = -1.0 + 2.0*center_x/x_resolution
then
rotation_to_target = target_x * camera_fov / 2.0
w
h
x,y
w
negative rotations
positive rotations
x,y
h
h
x,y
w
h
w
α